## Slide 1: CORA engine QuickBlocks
F. Kraaijeveld PTI/RC
Geomechanicist
Leakage along fault planes
Leakage through the cap rock
Leakage along wells
Lateral Migration:
Subsidence

## Slide 2: Quickblocks setup model
  All components need to be added upfront. No update possible.
  Model setup:
    To generate input form
      Choose template or model (filename will be asked after “Generate input form”)
      Choose component input forms
      Choose name output folder (will be created at level of Excel sheet)
      Generate input form (and choose model)
    Fill in base case, including component details
    Fill in uncertainties
    Set up correlation matrix
    Validate & continue
  You can select and deselect uncertainties & components
  Always validate after a change

## Slide 3: Quickblocks features
Input model
  via template (4 layers, dP): basecase + uncertainties
  QB 2.* model: only uncertainties. Note that even if mean distribution is not equal to basecase value, the mean is used.
  Settings sheet to set path to EPD & QB

## Slide 4: QuickBlocks limitations in cora
  Template
  4 Horizontal layers
  Only pressure depletion, temperature changes not supported
  Models QuickBlocks version 2.*
  Formations with constant depths (not arrays or pointset due to identification of (failure) material contrasts), incl surfacedepth.constant
  Only parameters that are a Real are allowed to have uncertainty assigned
  Failure modes
  Failure area = sum failed points times grid size (irrespective thickness layer)
  Fault is a plane
  Formation is a volume
  Well is a line
  Subsidence always at surfacedepth (not yet validated in GUI)

## Slide 5: CORA QB IO workflow
  This holds for each calculation case
  Objective
    Input: interfacing ascii file with settings and parameters
    Output: QB inputfile, results file and/or single LSV per case
  Architecture:
    QBcreatecase.py:
    Transfers case ascii file to QB input file by updating properties for a known model, including output properties (pointset, depths, propout).
    QBruncase.py:
    Runs QB core with created file using settings in ascii file in multiprocessing or normal mode
    Currently VBA Possibly: QBevalcase.py (being replaced by more general code): Calculate LSV based on resistance and QB results
=
Post-processing
QuickBlocks
Pre-processing
Model

## Slide 6: Formations
Failure modes
  Shear failure (SCU from principal stresses)
  Tensile failure (min principal stress)
  Later: Pore collapse (max principal stress)
  Compression failure (max principal strain)
  Extension failure (min principal strain)
  Compaction failure (max Ez)
  Later: Elongation failure (min Ez)
Types
  Volume G
  Gridplanes
  Formation name
  Note: only gridplanes rotates volume with blocks (blocks.angle <>0)

## Slide 7: Faults
Failure modes
  Shear failure (rotated stresses for full element set)
Types
  Template
  GoCad file (.mx)

## Slide 8: Wells
Failure modes
  Later: Shear failure (see formation)
  Later: Tensile failure (see formation)
  Axial compression
  Axial extension
Types
  Template
  Not tested: 3D pointset file

## Slide 9: Subsidence
Failure modes
  Subsidence
  Later: Upheave
Type
  Gridplane @ surface
  Later: pointset @ surface

## Slide 10
Background information QuickBlocks PRE- & post-processing

## Slide 11: In situ stress
Sv,SH,Sh to SNN,SEE,SDD system
Sv = SDD
SEE = 0.5[(SH + Sh )-(SH - Sh )cos(2azi)]
SNN = 0.5[(SH + Sh )+(SH - Sh )cos(2azi)]
SEE = 0.5(SH - Sh )sin(2azi)
N,y
E,x
azi
Sh
SH

## Slide 12: Component definitions in Qbmodi (1)
Formation
Template volume (see picture; segH,segV view discretization; sample for calculation depths)
Template gridplane (view points + depths)
Name (of formation/layer; segH,segV view discretization; sample for calculation depths)
N,y
E,x
D,z
height
widthE
widthN

## Slide 13: Component definitions in Qbmodi (2)
Well
The azimuth is angle from Northing clockwise
The dip is angle with vertical anticlockwise
Fault
The azimuth is direction ball rolls, wrt Northing
The dip is the angle with horizontal, clockwise
N,y
E,x
D,z
azi
dip
E,x
D,z
N,y
width
height
dip
azi

## Slide 14: Well path
N,y
E,x
D,z
azi
dip

## Slide 15: Fault planE
Center point
  HeartE = Egrid.min()+(Egrid.max()-Egrid.min())/2.
  HeartN = Ngrid.min()+(Ngrid.max()-Ngrid.min())/2.
  HeartD = Dgrid.min()+(Dgrid.max()-Dgrid.min())/2.
Vectors
  Normal = [np.sin(dip)*np.cos(azi), np.sin(dip)*np.sin(azi), -np.cos(dip)]
  Shear = [np.cos(dip)*np.cos(azi), np.cos(dip)*np.sin(azi), np.sin(dip)]
  Strike = [-np.sin(azi), np.cos(azi), 0]
E,x
D,z
N,y
width
height
dip
azi

## Slide 16: Workflow Fault evaluation
Failure mechanism: Fault SCU
Input: fault shape, fault cohesion, fault friction angle
Output: SCU ave, SCU max, SCU area m^2, SCU area %
Template
GoCad file
QB psfile
VBA
CORA
QB input file
QB results file
n,t per segment
SCU ave and max
C#
python
QB psfile
GoCad file
Intermediate file