## Slide 1: CORA methodologies
Famke Kraaijeveld PTI/RC
Leakage along fault planes
Leakage through the cap rock
Leakage along wells
Lateral Migration:
Subsidence

## Slide 2
Leakage along fault planes
Leakage through the cap rock
Leakage along wells
Lateral Migration
Subsidence

## Slide 3
Distribution functions & proxys

## Slide 4: DiStribution functions
Deterministic : No stochastic distribution
Normal : Exponential / Bell shape
LogNormal : Shifted normal distribution
Uniform : Block shape, 1 between min and max value X
TruncatedNormal: Normal with cut-off, s.t. area = 1, i.e. Mean might change
Uniform
Normal
Lognormal
Lognormal

## Slide 5: Proxys for responses
FirstOrderProxy P10: Single plane (from P10 and P50)
FirstOrderProxy P90: Single plane (from P50 and P90)
FirstOrderDoubleProxy: Double plane (P10, P50 and P90),
connecting at basecase
SecondOrderProxy: Second order surface (P10, P50 and P90)
ExperimentalDesign: Least square fit of single plane (P10, P50 and P90)

## Slide 6: correlations
Source:
http://en.wikipedia.org/wiki/Correlation_and_dependence
Value from [-1,1]
Fully correlated means 1-on-1 relation, i.e. the dependent stochast is known main stochast is sampled.

## Slide 7
Reliability methods

## Slide 8: Material & Operational failure
Proxies are based on responses
Response = Max, mean, fail area, fail area %
  Failure area and failure area % are the result of material failure
  Material failure is defined as component property, e.g. SCU = 1, S3Min, E1 Max, Uz Max (Uz Max = 0 gives subsidence bowl)
  Reliability is based on operational failure:
  LSF = Z-function = resistance – response
  Resistance = operational limit, e.g. Uz % failure area = 0.2, SCU = 1.1, Uz max
  Negative resistances, tensile failure, might give issues

## Slide 9: Reliability methods
Methods:
  First Order Residual Method (FORM) : For best performance
  MonteCarlo (MC): Gives most precise results, but takes lots of time
  DirectionalSampling (DS): Intermediate solution
  ImportanceSampling (MIS): Intermediate solution
  NumericalIntegration (NI): Solution by integrating values, might be added later

## Slide 10: Reliability methods
Parameters to control the probabilistic computation
Probabilistic Parameter | Methodology | Description
Seed | MonteCarlo, ImportanceSampling, DiretionalSampling | Seed value for randomizer
Umin, Umax | NumericalIntegration | Minimum and maximum value for u, only used in numerical integration
Intervals | NumericalIntegration | Number of intervals in numerical integration
MinimumSamples, MaximumSamples | MonteCarlo, ImportanceSampling, DiretionalSampling | Minimum and maximum samples in MC, DS, MIS
MaximumIterations | FORM | Maximum number of iterations in FORM
StartMethod | FORM | Start method for FORM, possible values: StartZero, StartOne, StartGivenVector, StartRaySearch, StartSphereSearch
StartVector | FORM | Start values for u in FORM, When supplied, the StartMethod is set to StartGivenVector.
RelaxationFactor | FORM | Relaxation factor for FORM
VarianceFactor | MonteCarlo, ImportanceSampling | Variance factor for Importance Sampling
VariationCoefficientFailure, VariationCoefficientNoFailure | MonteCarlo, ImportanceSampling | Required variation coefficient for failure and non failure
Threshold Relaxation Factor | All | Relaxation factor for lowering the threshold for switching between the proxy and the real engine

## Slide 11: form
  Estimated by
    transfer to normal distributions
    Linearized z-function
  Fast

## Slide 12: Crude monte carlo
  “Random sampling”
  P = # failed/ total
  Stops when variance small (convergence) or max samples
  Most precise

## Slide 13: MC Importance sampling
  Sampling towards failure cases
  P = weighted (# failed, total)
  Stops when variance small (convergence) or max samples
  Captures local minimum, i.e. requires pre-knowledge

## Slide 14: MC directional sampling
  Sampling in directions to find failure plane
  Probability from transfer to nomally distributed PDFs
  Assumes LSF function) monotone and smooth
  Faster than crude

## Slide 15: Numerical integration
  Sampling by discretizing the stochast
  Probability of failure from summation of all failure combinations

## Slide 16: Automatic switch in reliability methods
When LSF = Resistance - Response < Threshold then
Switch to engine
Update proxy
Lower threshold by 2/3
Note:
  Threshold = 0 means only proxy calculations
  Factor could be made input parameter
  Update proxy y/n could be steered from xml

## Slide 17: Reliability results
Reliability:
  Beta
  Probability of failure
  Design point
  FORM: direct;
  MC: centre of gravity or methods of angles
  In u-space (standard Normal distributions)
  Defined by
    Alpha: coefficient
    U: normalized design point
    X: design point
Notes: Standard normal Bell-shaped curve and the associated standard deviations and
cumulative percentiles. The reliability index is represented by the Standard
Deviations.

## Slide 18: System reliability
Failure occurs only if all components fail: Parallel system of components
If components are independent:
PFail = PF1* PF2
Failure occurs if one or more components fail: series of components
If components are independent:
PFail = 1 – (1-PF1) * (1-PF2)
1
2
If PF1 and PF2 are small
 PF1 + PF2
1
2
1
2
3
PFail = PF1* [1 – (1-PF2) * (1-PF3)]
If components are independent:

## Slide 19: System reliability
System reliability based on combined response surfaces
  Directional sampling
  Using design point per component
  When components are independent and have probability of non-failure of P1, P2, ..., then system failure equals
  Probability of failure = 1-(1-PF1)*(1-PF2) *… = PF1 + PF2+ ...
  Probability of non failure = P1*P2*…
Reliability (Test03dualzoneproducinginterval1.Initial.Initial.Resistance=0Test03dualzoneproducinginterval2 .Initial.Initial.Resistance=0, (MonteCarlo) |  |  | 
 | Test03dualzoneproducinginterval1 .Initial.Initial | Test03dualzoneproducinginterval2 .Initial.Initial | System
Beta | 0.410664445 | -0.25696902 | -1.751071457
Probability of failure | 0.340659341 | 0.601398601 | 0.960033242
Probability of non failure | 0.659340659 | 0.398601399 | 0.039966758